## Slide 1
KUBERNETES-NATIVE 5G PLATFORM
RAN Architecture Evolution
Six architectures on one Open5GS core — with throughput, latency and
capacity measured end-to-end through each one.
292-339
Mbit/s across scenarios
~10 ms
RTT, every architecture
6×
edge latency advantage
17,289
retransmits at the ZMQ limit
Advanced Communications & Networks Research · Open Source 5G Platform
Notes: All figures on this slide are measured on the platform, not vendor claims. Method is on the performance slides.

## Slide 2
AGENDA
Six Architectures, One Core
Each model changes how RAN functions are split, placed and scaled — never what the core provides.
01
Centralized RAN (C-RAN)
Monolithic gNB — the traditional baseline
02
Disaggregated RAN (O-RAN)
CU/DU split over the standardized F1 interface
03
Cloud-RAN
BBU functions virtualized in a shared compute pool
04
Virtualized Cloud-RAN (v-CRAN)
The CU as an elastic, autoscaled workload
05
Heterogeneous Cloud-RAN (H-CRAN)
Macro coverage + small-cell capacity, coordinated
06
Fog RAN (F-RAN)
Processing pushed to the edge for local breakout
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
02 / 24

## Slide 3
C-RAN
Centralized RAN
The traditional baseline — every gNB function in one process.
01
i
Definition
All baseband functions — PHY, MAC, RLC, PDCP and RRC — run as one monolithic process co-located with, or directly wired to, the radio. Nothing is split across a network interface.
e
Example in this platform
A single srsRAN or OAI gNB binary handling the complete air interface for one cell, driving a radio directly.
c
Characteristics
Single process owns the entire air interface
Tight, sub-millisecond internal timing — no fronthaul network
Simple to configure: one binary, one config file
Typically single-vendor by construction
NETWORK ARCHITECTURE
UE
Handset / SIM
Radio Unit
USRP B210 (RF)
Monolithic gNB
CU + DU + PHY, one process
5G Core
Open5GS on Kubernetes
RF
USB / IQ
N2 / N3
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
03 / 24
Notes: Real-radio path measured separately; the ZMQ variant shares the throughput profile of the other simulated scenarios.

## Slide 4
C-RAN
Centralized RAN
Advantages, trade-offs, and where it is used in industry
01
+
Advantages
Fewest moving parts — easiest to deploy and debug
Lowest possible latency: no inter-function network hop
Straightforward capacity planning for a single cell
Ideal for labs, pilots and private-network trials
!
Trade-offs
No resource pooling — each cell reserves its own compute, even when idle
Scaling means adding whole gNBs, not just the busy layer
Effectively single-vendor per site
Wastes capacity at low load, a hard ceiling at high load
HOW IT'S ADDRESSED
Virtualizing the BBU into a shared pool (Cloud-RAN) or splitting the CU from the DU (O-RAN) are the two paths out of this ceiling — both covered next.
n
Where it's used in industry
The default model for early 4G/5G NSA rollouts
Still the right choice for private 5G / campus networks
Common in labs and RF-development testbeds
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
04 / 24

## Slide 5
O-RAN
Disaggregated RAN
Splitting the gNB into interoperable CU and DU functions.
02
i
Definition
The gNB is split at a standardized point: the DU keeps the real-time PHY/MAC/RLC layers near the radio, the CU centralizes RRC/PDCP, and the two talk over the O-RAN Alliance's F1 interface.
e
Example in this platform
srsRAN's and OAI's own CU and DU images run as separate Kubernetes Deployments, connected over F1-C/F1-U through a Service.
c
Characteristics
Standardized F1 (CU-DU), E1 (CU-CP/CU-UP) and O1 interfaces
DU stays real-time and cell-bound; CU can be centralized
Opens the door to a RAN Intelligent Controller (RIC)
Interfaces are open — components need not share a vendor
NETWORK ARCHITECTURE
RU
Radio (simulated)
DU
PHY / MAC / RLC
CU
RRC / PDCP
5G Core
RF
F1
N2 / N3
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
05 / 24
Notes: Throughput and latency for this architecture are on the ten-combination matrix slide.

## Slide 6
O-RAN
Disaggregated RAN
Advantages, trade-offs, and where it is used in industry
02
+
Advantages
No single-vendor lock-in — CU and DU can come from different suppliers
CU and DU scale independently of each other
Centralizing the CU enables coordination across many DUs
Drives cost down through vendor competition
!
Trade-offs
Multi-vendor interoperability testing is a real, ongoing burden
F1 adds a network hop the monolithic design didn't have
The wider multi-vendor ecosystem is still maturing in practice
HOW IT'S ADDRESSED
O-RAN Alliance conformance and interoperability test specs exist to close this gap; most operators start single-vendor and diversify once conformance is proven.
n
Where it's used in industry
Rakuten Mobile — first large-scale commercial Open RAN network
Dish Network's greenfield 5G build
Vodafone, AT&T and Verizon OpenRAN trials and deployments
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
06 / 24

## Slide 7
CLOUD-RAN
Cloud-RAN
Virtualizing baseband into a shared, centralized compute pool.
03
i
Definition
Baseband processing runs as software in a centralized pool on general-purpose (COTS) hardware, serving many remote radio sites at once, instead of dedicated appliances at every site.
e
Example in this platform
helm/cloud-ran-srsran and cloud-ran-oai deploy the gNB as an ordinary Kubernetes workload — CPU/memory requests, ConfigMap-driven, no bespoke hardware.
c
Characteristics
Statistical multiplexing: one pool absorbs many sites' variable load
Runs on commodity servers, not proprietary baseband hardware
Centralized software lifecycle — one place to patch and upgrade
Per-cell QoS (5QI) profiles configured centrally
NETWORK ARCHITECTURE
Remote Radio
RRU at the tower
Fronthaul
Transport network
Virtualized BBU Pool
Kubernetes, COTS compute
5G Core
fiber
fronthaul
N2 / N3
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
07 / 24
Notes: Shares the simulated-radio data path; throughput tracks the O-RAN and v-CRAN figures.

## Slide 8
CLOUD-RAN
Cloud-RAN
Advantages, trade-offs, and where it is used in industry
03
+
Advantages
Pooling cuts total compute versus one appliance per site
Multi-cell coordination becomes possible from one location
Centralized monitoring, upgrades and fault management
Materially lower total cost of ownership at scale
!
Trade-offs
Fronthaul must meet strict latency and bandwidth budgets
The centralized pool is a concentration-of-risk point
Every remote site depends on reliable, high-bandwidth transport back to the pool
HOW IT'S ADDRESSED
Redundant fronthaul paths, and lower-bandwidth functional splits (e.g. split 7.2) that relax the transport requirement while keeping the pooling benefit.
n
Where it's used in industry
China Mobile — originated the C-RAN concept at scale
Standard pattern for dense urban 5G capacity buildouts worldwide
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
08 / 24

## Slide 9
V-CRAN
Virtualized Cloud-RAN
The CU as an elastic, autoscaled Kubernetes workload.
04
i
Definition
Takes Cloud-RAN further: the CU is not just virtualized but actively managed — replica count, resource limits and placement are all governed by the orchestrator and respond to real load.
e
Example in this platform
The CU carries a HorizontalPodAutoscaler (1-3 replicas, 70% CPU target) plus soft pod anti-affinity; the DU stays fixed, bound to its cell and real-time deadlines.
c
Characteristics
Elasticity: replica count follows measured CPU load automatically
Explicit resource governance — requests and limits per replica
Placement policy spreads replicas across nodes where possible
Entire lifecycle expressed declaratively in one Helm chart
NETWORK ARCHITECTURE
DU
fixed · 1 replica
F1
CU
CU
CU
CU POOL — HPA: 1-3 replicas @ 70% CPU
N2/N3
5G Core
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
09 / 24
Notes: Throughput and latency for this architecture are on the ten-combination matrix slide.

## Slide 10
V-CRAN
Virtualized Cloud-RAN
Advantages, trade-offs, and where it is used in industry
04
+
Advantages
Capacity tracks real-time demand instead of worst-case provisioning
Idle capacity is reclaimed automatically between busy periods
Anti-affinity improves resilience to a single node failing
Fully cloud-native operational model — same tooling as any other workload
!
Trade-offs
F1's SCTP association is long-lived — scaling out doesn't rebalance a DU already connected
A combined CU (not split into CU-CP/CU-UP) limits how far user-plane load alone can scale
On a single node, autoscaling is bounded by whatever capacity is left
HOW IT'S ADDRESSED
Production systems split CU-CP and CU-UP over E1 so only the user plane — the part that scales with traffic — needs extra replicas; a multi-node cluster removes the single-node ceiling.
n
Where it's used in industry
The direction 5G RAN cloudification is heading industry-wide
Rakuten Symphony and major telco-cloud offerings orchestrate RAN this way
Active area of Kubernetes-based RAN orchestration research
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
10 / 24

## Slide 11
H-CRAN
Heterogeneous Cloud-RAN
Macro coverage plus small-cell capacity, coordinated centrally.
05
i
Definition
A wide-coverage macro cell anchors control and mobility, while small cells absorb local traffic demand — the cells differ deliberately in power, bandwidth and coverage radius, coordinated by one cloud-hosted core.
e
Example in this platform
One 'macro' gNB (PCI 1, higher tx power, lower compute) and one 'small' gNB (PCI 2, lower tx power, higher compute), both attached to the same AMF at once.
c
Characteristics
Deliberately heterogeneous cell tiers, not identical repeated cells
Macro carries control/mobility; small cells carry local data traffic
Requires coordinated scheduling to limit inter-cell interference
One shared cloud-hosted core serves every tier
NETWORK ARCHITECTURE
Macro Cell wide coverage · control anchor
Small Cell local capacity · higher compute
Shared Cloud Core
one AMF, both tiers
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
11 / 24
Notes: Throughput and latency for this architecture are on the ten-combination matrix slide.

## Slide 12
H-CRAN
Heterogeneous Cloud-RAN
Advantages, trade-offs, and where it is used in industry
05
+
Advantages
Adds capacity exactly where it's needed without new macro towers
Fills indoor and coverage dead-zones cheaply
Small cells cost and draw far less power than another macro site
Central coordination reduces interference between tiers
!
Trade-offs
True dual connectivity (one device on both cells at once) needs EN-DC/NR-DC support most simulators don't provide
More cells directly means more day-to-day management overhead
Careful RF planning is required to avoid the tiers interfering
HOW IT'S ADDRESSED
Dual-connectivity-capable RAN stacks provide full EN-DC/NR-DC; automated SON tooling handles interference coordination at production scale.
n
Where it's used in industry
Small-cell overlays on the macro grid — standard practice for every major operator
Stadiums, campuses and dense urban hotspots for capacity augmentation
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
12 / 24

## Slide 13
F-RAN
Fog RAN
Pushing processing to the edge for genuine local breakout.
06
i
Definition
Traffic that can be served locally never traverses the central core at all: a dedicated edge UPF with its own DNN and no internet route hands sessions directly to an application co-located at the edge.
MEASURED ON THIS PLATFORM
~0.8 ms
edge DNN
~5.0 ms
internet DNN
6×
faster locally
TCP connect time, edge DNN vs internet DNN, same UE.
c
Characteristics
Local breakout: a per-DNN decision, not a blanket routing change
MEC application co-located with the edge UPF
Ordinary internet traffic is unaffected and still routes centrally
Latency gain comes from removing hops, not adding bandwidth
NETWORK ARCHITECTURE
RAN
Edge UPF — NAT off
Edge App (MEC) · ~0.8 ms
Central UPF
Internet · ~5.0 ms
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
13 / 24

## Slide 14
F-RAN
Fog RAN
Advantages, trade-offs, and where it is used in industry
06
+
Advantages
Minimum latency for latency-critical apps (AR/VR, industrial control, gaming)
Removes that traffic's load from backhaul and the central core entirely
Data can stay on-site for locality or privacy requirements
Central core stays lean, sized for what actually needs to leave the site
!
Trade-offs
An edge UPF with nothing running at the edge accomplishes nothing
Edge sites need their own compute and their own operations
A single-node lab can't show the real distance-driven latency gain
HOW IT'S ADDRESSED
This is the ETSI MEC pattern: always pair edge UPF placement with a genuine local workload — a cache, an industrial controller, an AR renderer — and validate on a real multi-site topology.
n
Where it's used in industry
Verizon, AT&T and Rakuten MEC deployments for stadiums, factories and live events
Industrial private 5G networks needing deterministic low latency
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
14 / 24

## Slide 15
PERFORMANCE
Measured, Not Assumed
Every figure taken end-to-end through the UE's own PDU session — traffic genuinely traverses RAN, core and UPF.
M
Method
iperf3 server on the host's cni0 bridge; client run inside the UE pod, source-bound to its tunnel interface so traffic cannot shortcut the RAN or core.
Latency measured with ping over the same tunnel to a public internet destination (8.8.8.8), 15-20 packets per run.
Identical procedure for every scenario, so the numbers are comparable rather than anecdotal.
Chart: Sustained throughput, 10s single stream
| O-RAN + OAI | v-CRAN + OAI | H-CRAN + OAI
Throughput (Mbit/s) | 320 | 339 | 292
All three architectures land in the same 292-339 Mbit/s band at ~10 ms RTT.
That is the expected result, and worth stating plainly: splitting the gNB (O-RAN), autoscaling the CU (v-CRAN) or attaching a second cell (H-CRAN) changes how the RAN is deployed and managed — it does not change the data path a single UE's traffic actually takes.
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
15 / 24

## Slide 16
FINDING
What the Autoscaler Actually Responds To
v-CRAN's HPA never moved under a sustained throughput test — and that is the correct behaviour.
339 Mbit/s
sustained through the CU/DU path
Bulk user-plane traffic, pushed for a full 10 seconds.
3-4% / 70%
HPA utilisation vs target
Flat throughout. No scale-out, no scale-in, no movement at all.
18m / 216m
CU vs DU CPU under load
The DU forwards the payload; the CU stays essentially idle.
Why: the CU is a receptionist, not a delivery driver.
The CU handles RRC and PDCP control signalling — registration, session setup, mobility. Once a session is established, the DU and UPF carry the actual packets. So more data from one UE creates almost no additional CU work, and an HPA watching CU CPU correctly stays flat.
Scaling this CU would need concurrent control-plane load — many UEs registering or handing over at once — not more traffic volume from a single UE. Testing the wrong kind of load is the common mistake here; the flat result is evidence the autoscaler is scoped correctly.
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
16 / 24

## Slide 17
MATRIX
Every Architecture, Both Stacks
Five architectures × srsRAN and OAI — ten combinations, one identical test procedure.
Architecture | srsRAN Mbit/s | srsRAN RTT ms | srsRAN retr | OAI Mbit/s | OAI RTT ms | OAI retr
C-RAN | 205 * | 8.84 | 339 | 287 | 9.04 | 463
O-RAN (CU/DU over F1) | 215 | 8.23 | 313 | 302 | 8.17 | 419
Cloud-RAN | 199 | 8.69 | 253 | 295 | 9.63 | 400
H-CRAN (macro + small) | 147 | 8.35 | 195 | 304 | 8.34 | 402
v-CRAN (autoscaling CU) | 222 † | 9.95 | 337 | 343 † | 8.53 | 500
* C-RAN + srsRAN drives a real USRP B210 rather than the ZMQ simulator, so it is not directly comparable to the other nine.
† v-CRAN re-measured after the sweep; see the caveat below.
Read these as indicative, not definitive.
All ten ran back-to-back on one node in a single session, so later scenarios were measured on a busier machine than earlier ones — throughput tracks run order as much as architecture. v-CRAN first read 130 and 117 Mbit/s at the end of the sweep; re-measured on a quieter node it gave 343 and 222, matching an independent earlier reading of 339. Separating architecture from load would need each scenario measured from the same idle baseline.
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
17 / 24

## Slide 18
COMPARISON
Six Models, Side by Side
Same building blocks — CU, DU, radio, core — arranged and scaled differently.
Dimension | C-RAN | O-RAN | Cloud-RAN | v-CRAN | H-CRAN | F-RAN
Splits functions? | No — monolithic | Yes — CU / DU (F1) | No, but virtualized | Yes, CU elastic | By cell tier | By traffic locality
Scales by | Adding whole gNBs | CU / DU independently | Pool sizing | Autoscaler (HPA) | Adding small cells | Adding edge sites
Latency profile | Lowest (no split) | Low + F1 hop | Fronthaul-bound | Fronthaul-bound | Per-tier | Lowest at the edge
Measured RTT | — | ~10 ms | — | ~10 ms | ~10 ms | ~0.8 ms (edge)
Measured throughput | — | 320 Mbit/s | — | 339 Mbit/s | 292 Mbit/s | —
Vendor flexibility | Single vendor | Multi-vendor (F1) | Single/multi | Single/multi | Single/multi | Single/multi
Best for | Labs & private nets | Avoiding lock-in | Urban densification | Variable, bursty load | Hotspot capacity | Latency-critical apps
Highlighted rows are measured on this platform. Dashes mark scenarios whose data path is shared with a measured one, or measured differently (F-RAN uses TCP connect time).
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
18 / 24

## Slide 19
RECOMMENDATION
Which One Is Better?
There isn't a single winner — each model answers a different question.
C-RAN
Choose when simplicity matters most
Labs, pilots, private/campus 5G — nothing to coordinate, nothing to debug across a network hop.
O-RAN
Choose to avoid vendor lock-in
Multi-vendor sourcing, or preparing for RIC-based optimization later.
Cloud-RAN
Choose for large-scale density
Many sites, centralized ops, fronthaul that meets the latency budget.
v-CRAN
Choose for bursty control-plane load
Many UEs attaching and handing over — not simply more traffic from few UEs.
H-CRAN
Choose for hotspot capacity
Stadiums, campuses, dense pockets — without building another macro site.
F-RAN
Choose for latency-critical apps
Measured 6× faster to a local service than out through the central path.
In practice these aren't mutually exclusive.
All six run on one Open5GS core and switch from a single scenario dashboard — evidence that the choice of RAN architecture is a deployment and orchestration decision, not a redesign of the core.
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
19 / 24

## Slide 20
SUMMARY
Key Takeaways
1
Function placement is the real variable
Every model uses the same CU/DU/PHY building blocks — what changes is where each function runs and how it is scaled.
2
Deployment shape did not change the data path
O-RAN, v-CRAN and H-CRAN all measured 292-339 Mbit/s at ~10 ms. Splitting or autoscaling the RAN changes operations, not one UE's throughput.
3
Autoscaling must target the right load
The CU's HPA stayed flat at 3-4% under a full-rate transfer, because the CU does signalling, not forwarding. Scaling it needs concurrent registrations.
4
Edge value is measurable, and it comes from removing hops
~0.8 ms to a local MEC app versus ~5.0 ms out through the central path — a 6× advantage even with no physical distance involved.
5
Know which limit you are hitting
Four parallel streams cut throughput and raised retransmits 39× while both pods sat under 3% CPU — the ceiling was the ZMQ simulator, not the design.
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
20 / 24

## Slide 21
ADDENDUM
Deployment & Infrastructure
How each architecture was actually built on Kubernetes, and the problems solved along the way.
Included for infrastructure engineers; not required to follow the architectural comparison.
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
21 / 24

## Slide 22
ADDENDUM
Build Notes
C-RAN and O-RAN — implementation and problems solved
01 Centralized RAN
K
How we built it
Bare-metal srsRAN gNB (all layers) driving a USRP B210 directly
Equivalent Kubernetes chart using a ZMQ-simulated radio for the six-way comparison
?
Challenges solved
B210's free-running clock drifts, causing radio-link failure after 90-140s of a real over-the-air session — traced by elimination (USB, core timers, thermal, CPU pinning all ruled out) to the missing external clock reference
Getting the UE's requested slice (NSSAI) to match across the subscriber record, the gNB and the AMF simultaneously — the allowed slice is the intersection of all three
02 Disaggregated RAN
K
How we built it
helm/srsran-oran and helm/oai — each a cu/ and du/ chart pair
DU resolves the CU via a Kubernetes Service DNS name at startup
?
Challenges solved
The DU resolves the CU exactly once at startup with no retry — if the CU isn't up yet, the DU bakes an empty address into its config and fails with an obscure parse error rather than waiting
OAI's CU shipped an e2_agent block pointing at a RIC that was never deployed, retrying E2 SETUP forever — harmless to the data path, but removed to keep the logs clean
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
22 / 24

## Slide 23
ADDENDUM
Build Notes
Cloud-RAN and v-CRAN — implementation and problems solved
03 Cloud-RAN
K
How we built it
gNB as a Kubernetes Deployment with an init script that substitutes PLMN/AMF/TAC into the config at container start
Full TS 23.501-based 5QI-to-bearer QoS profile set shipped with the chart
?
Challenges solved
Sizing CPU/memory requests for a software modem — too tight and the pod is OOMKilled, too loose and pooling gains nothing
Getting the sed-based config substitution (PLMN, AMF address, TAC) to run reliably before the gNB process starts, every time the pod restarts
04 Virtualized Cloud-RAN
K
How we built it
Forked the O-RAN CU/DU charts (srsRAN and OAI) and added an HPA, resource requests/limits and pod anti-affinity to the CU only
Installed metrics-server (--kubelet-insecure-tls on kubeadm) so the HPA has real CPU data to act on
?
Challenges solved
The CU was OOMKilled at a 2Gi memory limit — needed 4Gi; found only by reading the pod's termination reason, not the application log
Watched the HPA read 104-107% against its 70% target and scale 1 → 2 replicas entirely on its own — the autoscaling loop working end to end
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
23 / 24

## Slide 24
ADDENDUM
Build Notes
H-CRAN and F-RAN — implementation and problems solved
05 Heterogeneous Cloud-RAN
K
How we built it
One parameterized Helm chart (PCI, bandwidth, tx_gain, resources as values) deployed twice — once per tier — for both srsRAN and OAI
Both cells attach to the same core simultaneously, confirmed by the AMF's own gNB count
?
Challenges solved
10 MHz at 30 kHz subcarrier spacing failed srsRAN's own validation (PUCCH would exceed 50% of the channel) — both cells run 20 MHz and differentiate by power and compute instead, arguably the more realistic choice
OAI cross-references its gNB by name in several config fields at once — renaming one cell without updating all of them made the softmodem assert a mismatch and exit
06 Fog RAN
K
How we built it
A dedicated edge DNN (10.47.0.0/16) with its own tunnel interface and NAT disabled, added to the SMF and UPF
A small nginx MEC application reachable only through that edge session
?
Challenges solved
The SMF's advertised DNN list had to include the new DNN explicitly, or the AMF rejected the session with PAYLOAD_NOT_FORWARDED
Proved genuine local breakout two ways: the edge app's access log recorded the handset's real unmasqueraded address rather than a NAT'd cluster address, and the same session could not reach the internet at all
5G RAN ARCHITECTURES · MEASURED ON A KUBERNETES-NATIVE PLATFORM
24 / 24